## Slide 1
Datasheet|AX3000 Dual Band Gigabit Uplink Wi-Fi6 Wall AP
FR-WA22GP-3000W1
FR-WA22GP-3000W1 supports ieee802.11ax standard and is downward compatible with ieee802.11ac/n/g/b/a, providing wireless data transmission rate up to 3.0gbps, with the characteristics of fast speed, low delay, large capacity, more security and more power saving. Compared with the previous generation of Wi Fi, the connection rate and the total network capacity are greatly improved. Network delay, channel interference is reduced, data transmission efficiency and connection security are improved. In today's high-density, high congestion network environment, game delay is lower, 4K video experience is smoother, more suitable for a large number of smart home devices access. And support wall mounted design, very suitable for enterprises, hotels, airports, schools and other indoor or public places to achieve high-speed network coverage. At the same time, the product supports 802.3at standard power supply, which enables the AP to be installed even without AC power supply, reduces the installation cost, makes the installation and use more concise, convenient and flexible, and improves the traditional network layout.
Description
Major features
Support 802.11ax
High speed data rate up to 3000Mbps
2*1GE LAN Port(RJ45)
Support MU-MIMO and OFDMA
2*3dBi PCB Omnidirectional Antennas
Work temperature from 0 to 40℃
Supports up to 256 users for access (recommended concurrent access terminals: 60)
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
Notes: V 1.00 initial version

## Slide 2
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
Specification
Model | FR-WA22GP-3000W1
Chipset | MT7981B+MT7976CN+RTL8211FS
CPU | Dual-Core 1.3GHz
RAM | 256MByte(DDR3)
ROM | 16MByte(SPI Nor Flash)
External FEM | NO eFEM
Indicator | SYS
Port | 2*10/100/1000Mbps LAN Port(RJ45)
Button | 1*Reset
Antenna | 2*2.4G/5G 3dBi Dual-band PCB antennas
Power Supply | 802.3at/af
Dimension | 86*86*43mm
Installation | Wall-Mount
ESD | IEC61000-4-2, Level 3: Contact discharge: ±4kV, Air discharge: ±8kV
Surge | IEC61000-4-5, Common Mode 2kV
Temperature | Work：0~40℃ Storage：-40~70℃
Humidty | Work：10%~90% (RH non-condensing) Storage：5%~95% (RH without non-condensing)
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD

## Slide 3
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
Specification
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
Protocal | 5GHz:IEEE 802.11ax,IEEE 802.11ac,IEEE 802.11n,IEEE 802.11a 2.4GHz:IEEE 802.11ax,IEEE 802.11ac,IEEE 802.11n,IEEE 802.11g,IEEE 802.11b |  | 
Work Band | 2.4GHz & 5GHz |  | 
Wi-Fi Speed | 2.4GHz: Up to 574Mbps (2T2R) 5GHz: Up to 2402Mbps (2T2R) |  | 
Modulation | IEEE 802.11b:CCK, QPSK, BPSK IEEE 802.11g/a:OFDM IEEE 802.11n:QPSK, BPSK, 16QAM, 64QAM IEEE 802.11ac:BPSK, QPSK, 16QAM, 64QAM, 256QAM IEEE 802.11ax:BPSK, QPSK, 16QAM, 64QAM, 256QAM, 1024QAM |  | 
2.4G | Mode | Rate | Power(dBm)
 | 802.11b | 1M | 16±2dBm
 |  | 11M | 16±2dBm
 | 802.11g | 6M | 15±2dBm
 |  | 54M | 13±2dBm
 | 802.11n HT20 | MCS0 | 15±2dBm
 |  | MCS7 | 12±2dBm
 | 802.11n HT40 | MCS0 | 15±2dBm
 |  | MCS7 | 12±2dBm
 | 802.11ax HE-SU20 | MCS0 | 15±2dBm
 |  | MCS11 | 10±2dBm
 | 802.11ax HE-SU40 | MCS0 | 15±2dBm
 |  | MCS11 | 10±2dBm
5G | Mode | Rate | Power(dBm)
 | 802.11a | 6M | 15±2dBm
 |  | 54M | 13±2dBm
 | 802.11n HT20 | MCS0 | 15±2dBm
 |  | MCS7 | 12±2dBm
 | 802.11n HT40 | MCS0 | 15±2dBm
 |  | MCS7 | 12±2dBm
 | 802.11ac VHT20 | MCS0 | 15±2dBm
 |  | MCS9 | 11±2dBm
 | 802.11ac VHT40 | MCS0 | 15±2dBm
 |  | MCS9 | 11±2dBm
 | 802.11ac VHT80 | MCS0 | 15±2dBm
 |  | MCS9 | 11±2dBm
 | 802.11ax HE-SU20 | MCS0 | 15±2dBm
 |  | MCS11 | 10±2dBm
 | 802.11ax HE-SU40 | MCS0 | 15±2dBm
 |  | MCS11 | 10±2dBm
 | 802.11ax HE-SU80 | MCS0 | 15±2dBm
 |  | MCS11 | 10±2dBm

## Slide 4
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
Specification
HUNAN FULLRIVER HIGH TECHNOLOGY CO.，LTD
2.4G | Mode | Rate | RX Sensitivity(dBm)
 | 802.11b |  | 
 |  | 11M | -86dBm
 | 802.11g | 6M | -94dBm
 |  | 54M | -72dBm
 | 802.11n HT20 | MCS0 | -90dBm
 |  | MCS7 | -70dBm
 | 802.11n HT40 | MCS0 | -88dBm
 |  | MCS7 | -71dBm
 | 802.11ax HE-SU40 | MCS0 | -88dBm
 |  | MCS11 | -61dBm
5G | Mode | Rate | RX Sensitivity(dBm)
 | 802.11a | 6M | -93dBm
 |  | 54M | -72dBm
 | 802.11n HT20 | MCS0 | -89dBm
 |  | MCS7 | -70dBm
 | 802.11n HT40 | MCS0 | -86dBm
 |  | MCS7 | -68dBm
 | 802.11ac VHT20 | MCS0 | -86dBm
 |  | MCS9 | -64dBm
 | 802.11ac VHT40 | MCS0 | -83dBm
 |  | MCS9 | -61dBm
 | 802.11ac VHT80 | MCS0 | -81dBm
 |  | MCS9 | -59dBm
 | 802.11ax HE-SU20 | MCS0 | -86dBm
 |  | MCS11 | -64dBm
 | 802.11ax HE-SU40 | MCS0 | -83dBm
 |  | MCS11 | -60dBm
 | 802.11ax HE-SU80 | MCS0 | -81dBm
 |  | MCS11 | -59dBm