## Slide 1
FR-S5152GT-370P5 is a L3 managed 10G PoE switch. Provides forty-eight 10/100/1000Mbps self-adaption RJ45 port, plus four 10 gigabit SFP+ optical port, it can be used to link bandwidth higher upstream equipment. Using store-and-forward technology, combined with dynamic memory allocation, ensure the bandwidth effective allocation to each port. Special design a flow control, it can avoid packet loss effectively when nodes in the sending and receiving data. Easy to maintenance and management, meet the networking and access requirements of enterprises, intelligent village, hotel, office network and campus network. Built-in high reliability, design for wide voltage input application power supply, even if the voltage is not stable of power grid, also can guarantee the equipment can work normally.
FR-S5152GT-370P5 forty-eight ports have PoE power supply function, support IEEE802.3at standard, 802.3af downward compatibility, power supply equipment for Ethernet, can automatically detect identification standard of electrical equipment, and through the cable for the power supply.
Description
Features
Supports IEEE 802.3i 、IEEE802.3af、IEEE802.3at、IEEE 802.3u 、IEEE802.3z、IEEE802.3ab、IEEE802.3x、IEEE802.3ae、IEEE802.3az.
Supports PoE power up to 30W for each PoE port, all power up to 370W.
Supports MAC address auto-learning and auto-aging.
Forty-eight 10/100/1000Mbps self-adaption RJ45 port, plus four gigabit port 1000/10000Mbps SFP+ port, it can be used to link bandwidth higher upstream equipment.
Store and forward mode operates.
Web-based Management Support.
LED indicators for monitoring power, link/activity,PoE.
19 inches full metal iron shell and internal power adapter design, suitable for rack installation.
Datasheet|48 GE +4 SFP+ L3 Managed PoE Switch
FR-S5152GT-370P5
湖南恒茂高科股份有限公司
HUNAN FULLRIVER HIGH TECHNOLOGY CO.,LTD.
Notes: V 1.00 initial version

## Slide 2
Specification
Model |  | FR-S5152GT-370P5
Chipset |  | RTL9311+6*RTL8218D+6*RTL8238B
Standards |  | IEEE 802.3i、IEEE 802.3u、IEEE 802.3az、IEEE802.3af、IEEE802.3ae、IEEE802.3at、IEEE802.3z、IEEE 802.3x
Ports |  | 48 x 10/100/1000Mbps ports 4 x 1000/10000Mbps SFP+ ports 1 x Console port
Network Media(Cable) |  | 10Base-T: UTP category 3, 4, 5 cable (maximum 100m) 100Base-Tx: UTP category 5, 5e cable (maximum 100m) 1000Base-T: UTP category 5e, 6 cable (maximum 100m) 1000Base-X: MMF,SMF 10GBase-X: MMF,SMF
Transfer Method |  | Store-and-Forward
MAC Address Table |  | 32K
Switching Capacity |  | 176Gbps
Packet Forwarding Rate |  | 130.95Mpps
Packet Buffer |  | 16Mbits
Jumbo Frame |  | 12KBytes
PoE Ports(RJ45) |  | 1-48 ports compliant with 802.3at/af
Power Pin Assignment |  | 1/2(+),3/6(-)
PoE Budget |  | 370W
LED indicators | Per Device | SYS&Mode : Green
 | Per-Port | RJ45/SFP+：Green
 |  | PoE：Green
Power Supply |  | AC 100~240V, 50/60HZ, 444W internal power
Dimensions（L×W×H） |  | 440*330*44mm
ESD |  | IEC61000-4-2, Level 3: Contact discharge: ±6kV, Air discharge: ±8kV
Surge |  | IEC61000-4-5, RJ45 Common Mode 6kV Power Common Mode 4kV Power Differential mode 2kV
Environment |  | Operating Temperature: 0℃ ~ 45℃ Storage Temperature: -40℃ ~70℃ Operating Humidity: 10%~90% non-condensing Storage humidity: 5%~90% non-condensing
湖南恒茂科股份有限公司
HUNAN FULLRIVER HIGH TECHNOLOGY CO.,LTD.

## Slide 3
Port properties | Support system LED、Port configuration、Port statistics Support MTU、DDM
Management and maintenance | Support System information、user management Support SSH Support Telnet-Server、Telnet-Client、Telnet6-Server、Telnet6-Client Support ping、ping6 Support Tracert Support WEB management、SNMP、RMON Support Manage IP restrictions、Manage timeouts、Reboot
VLAN | Support 802.1Q Support vlan-mac、vlan-protocol、vlan-subnet Support QinQ Support vlan-swap、vlan-translate
Forwarding control | Support Mac address management Support flow-control、BandWidth-Control、DLF-Control、SLF-Control、ErrorPacket-Control
Mirror | Support mirror、remote_mirror
security features | Support Port isolation、storm-control Support MUSER Support ip-source-guard、arp anti-flood、arp anti-spoofing Support Prevent DOS attacks Support Discard-BPDU Support dhcp anti-attack
system reliability | Support LACP、RSTP、MSTP、STP、LBD
DHCP | Support dhcp-snooping、dhcp-server、dhcp-relay、dhcp-client Support option82、option60
L2 multicast | Support IGMP-Snooping Support Static multicast
System alarm | Support syslog、cpu alarm、port alarm
Link detection | Support LLDP
Time management | Support Static state time、SNTP-Client
ARP | Support ARP、ND、ARP-proxy
IPv4 | Support Ordinary VLAN interface、SuperVLAN interface、Loopback interface Support Static routing, Routing strategy Support RIP、OSPF、VRRP Support ip-def-cpu
IPv6 | Support Ordinary VLAN interface、SuperVLAN interface、Loopback interface Support Static route Support RIPng
Software
HUNAN FULLRIVER HIGH TECHNOLOGY CO.,LTD.